This documentation describes gpgmailencrypt 2.2.x
# What is gpgmailencrypt
gpgmailencrypt is an encrypting e-mail gateway that can encrypt e-mails.
It supports
* PGP/Inline
* PGP/Mime
* SMime
* encrypted PDF

It can be used normally as a script doing everything on command line or in daemon mode, where gpgmailencrypt acts as an encrypting smtp server.
It takes e-mails and if a encryption key exists for this user it will return the e-mail encrypted to another e-mail server.
The encryption method can be selected per user.
## Prerequisites
The following software needs to installed
- python3.x
- gnupg (I recommend version 2)
- openssl
For encrypted-PDF you need to install:
- email2pdf (https://github.com/andrewferrier/email2pdf)
- wkhtml2pdf (http://wkhtmltopdf.org)
- pdftk
- 7zip
# Installation
## General
There are 2 different ways to install gpgmailencrypt. Choose the one that suits you best.In both cases you need to have installed python3 setuptools (on Ubuntu it's 'sudo apt-get install python3-setuptools')
### Using pip
Install pip first (on Ubuntu its 'sudo apt-get install python3-pip')
The most easy way to install gpgmailencrypt is via pip:
sudo pip3 install gpgmailencrypt

### Installing the archive
After you've downloaded the package from https://github.com/gpgmailencrypt/gpgmailencrypt/releases
unzip the zip-package with unzip gpgmailencrypt-xxx.zip / or untar it / tar -xzf gpgmailencrypt-xxx.tar.gz

Then change in the directory and start installation with
sudo python3 ./setup.py install

## Daemon
Make the gpgmailencrypt init file writeable
sudo chmod 755 /etc/init.d/gpgmailencrypt

Create a user (gpg-mailencrypt) under which the daemon should run
sudo adduser gpg-mailencrypt

You can set the user in the file /etc/default/gpgmailencrypt. It should contain
USER="gpg-mailencrypt" / DIR=”/usr/local/bin”

# Configuration /etc/gpgmailencrypt.conf
To create a default configuration file create the conf file with:
gme.py -x >~/gpgmailencrypt.conf / sudo cp ~/gpgmailencrypt.conf /etc
sudo chown gpg-mailencrypt.root /etc/gpgmailencrypt.conf / sudo chmod 640 /etc/gpgmailencrypt.conf

## General
[default] / prefered_encryption = pgpinline #valid values are / #'pgpinline','pgpmime' or 'smime' / add_header = no #adds a X-GPGMailencrypt header to / #the mail / domains = #comma separated list of domain / #names, that should be encrypted, / #empty is all / spamsubject =***SPAM #Spam recognition string, spam will / #not be encrypted / output=mail #valid values are 'mail'or 'stdout' / locale=en #DE|EN|ES|FR|IT|NL|PL|PT|RU|SE / mailtemplatedir=/usr/share/gpgmailencrypt/mailtemplates / #directory where mail / #templates are stored / systemmailfrom=gpgmailencrypt@localhost # e-mail address used when sending / #system mails / alwaysencrypt=False #if True e-mails will be sent / #encrypted, even if there is no key. / #Fallback encryption is encrypted pdf

## PGP specific configuration
[gpg] / keyhome = /var/lib/gpgmailencrypt/.gnupg #home directory of public / #gpgkeyring / gpgcommand = /usr/bin/gpg2 / allowgpgcomment = yes #allow a comment string in the / #GPG file

## SMIME specific configuration
[smime] / keyhome = ~/.smime #home directory of S/MIME public key / #files / opensslcommand = /usr/bin/openssl / defaultcipher = DES3 #DES3|AES128|AES192|AES256 / extractkey= no #automatically scan e-mails and / #extract smime public keys to / #'keyextractdir' / keyextractdir=~/.smime/extract / [smimeuser] / smime.user@domain.com = user.pem[,cipher] #public S/MIME key file [,used cipher, / #see defaultcipher]

## PDF specific configuration
The e-mail text will be stored in an encrypted pdf, attachments in an encrypted zip-file with the same password.
[pdf] / email2pdfcommand=/usr/bin/email2pdf #path where to find email2pdf (needed #for creating pdfs, see #https://github.com/andrewferrier/email2pdf) / pdftkcommand=/usr/bin/pdftk #path where to find pdftk (needed for #encrypting pdf files / pdfdomains=localhost #a comma separated list of sender #domains, which are allowed to use #pdf-encrypt / passwordlength=10 #Length of the automatic created #password / passwordlifetime=172800 #lifetime for autocreated passwords in #seconds. Default is 48 hours

## Zip-specific configuration
The zip functionality is mostly used with the pdf feature. Nevertheless you can use it indepently to zip all attachments (zipatttachments=True).
[zip] / 7zipcommand=/usr/bin7za #path where to find 7za / defaultcipher=ZipCrypto #ZipCrypto|AES128|AES256 / compressionlevel=5 #1,3,5,7,9 with 1:lowest compression, #but very fast, 9 is / # highest compression, but very slow, #default is 5 / securezipcontainer=False #attachments will be stored in an #encrypted zip file. If this option is #true, #the directory will be also encrypted / zipattachments=False #if True all attachments will be #zipped, independent from the #encryption method

## Daemon specific configuration
[daemon] / host = 127.0.0.1 #smtp host / port = 10025 #smtp port / smtps = False #use smtps encryption / starttls = False #use starttls encryption / forcetls = False #communication (e.g. authentication) / #will be only possible after STARTTLS / sslkeyfile = /etc/gpgsmtp.key #the x509 certificate key file / sslcertfile = /etc/gpgsmtp.crt #the x509 certificate cert file / authenticate = False #users must authenticate / smtppasswords = '/etc/gpgmailencrypt.pw' #use smtps encryption

The gpgmailencrypt.pw has the following format (for the authenticate option see chapter 6.3.):
user1=password1 / user2=password2

 Don't forget to make the file readable only for the gpgmailencrypt user!
How the x509 certificate files can be created see:
https://www.e-rave.nl/create-a-self-signed-ssl-key-for-postfix

The ssl certificates will be needed for “starttls” and “smtps” mode.
What's the difference between starttls and smtps? / Both create and use a ssl encrypted communication channel. Smtps is the old version, where both sides use ssl from the start. Starttls connections first start unencrypted, then both sides switch to ssl after sending the “startTLS” command. / In doubt use the starttls variant.

If you set stattls and smtps at the same time in your configuration, then SMTPS will be used.
# Key Management
The following commands have to be used as the user, that is running gpgmailencrypt. Remember that in daemon mode this user is 'gpg-mailencrypt'. So for daemon mode you first have to change the user
sudo su – gpg-mailencrypt

## PGP
Add a PGP key to the public key ring
gpg --import publickey.gpg

## SMIME
Smime keys are stored in the directory ~/.smime per default. You have to create it if it does not exist. Each key is stored in a single file in pem-format.
Usually you get the smime.key file in a different format. To convert it use
openssl pkcs7 -print_certs -inform DER -in smime.p7s -out smime.pem

Let's say you get the smime.p7s from agentj@mib.
Instead of 'smime.pem” you should use a unique name for the file and copy it in ~/.smime/
cp smime.pem ~/.smime/agentj@mib.pem

For this user you need also an entry in /etc/gpgmailencrypt.conf
[smimeuser] / agentj@mib = agentj@mib.pem

## Using PDF encryption
Let's say you want to send an e-mail with confidential content to somebody, but you don't have the gpg or smime key of the receiver. So PDF encryption is for you.
PDF encryption is -in contrary to gpg and smime encryption – a symmetric encryption method. Gpgmailencrypt is converting the e-mail text to a PDF file and puts all attachments in a ZIP file.
Both are encrypted with a password.
How to use PDF encryption? / Simply add #encrypt at the beginning of the subject of your e-mail (at least one whitespace after #encrypt). / That's all. / When you send your e-mail you will receive an automatic e-mail with the password. Give the password to the e-mail recipient via a different communication channel (e.g. phone). Then he can read the e-mail and the attachments with standard tools like a pdf-reader and any zip-application. / If the recipient has already a gpg or smime key, then this will be used.

# Integrating gpgmailencrypt in postfix
## Direct way from postfix to gpgmailencryt

Install and configure gpgmailencrypt as daemon.
/etc/gpgmailencrypt.conf
[mailserver] / host = 127.0.0.1 / port = 10025 / [daemon] / host = 127.0.0.1 / port = 10028

/etc/postfix/main.cf
content_filter=gpgmailencrypt:[127.0.0.1]:10028

/etc/postfix/master.cf
localhost:10025 inet n - n - - smtpd / -o content_filter= / -o mynetworks=127.0.0.0/8 / -o receive_override_options=no_unknown_recipient_checks / -o smtpd_recipient_restrictions=permit_mynetworks,reject_unauth_destination / -o smtpd_authorized_xforward_hosts=127.0.0.0/8 / gpgmailencrypt unix - - n - 2 smtp / -o smtp_data_done_timeout=1800

## From Postfix to amavisd to gpgmailencrypt
This is to check for viruses and spam before encrypting the mail

This has to be configured as before, except:
/etc/postfix/main.cf
content_filter=amavis:[127.0.0.1]:10024

/etc/postfix/master.cf
amavis unix - - n - 2 smtp / -o smtp_data_done_timeout=1800

/etc/amavis/conf.d/50-user
[...] / $notify_method = 'smtp:[127.0.0.1]:10028'; / $forward_method = 'smtp:[127.0.0.1]:10028';

Of course you have to configure amavisd to suite your needs.
Amavis and SSL / Amavis does not support SSL encryption of any kind or authentication. So you can't use these features of gpgmailencrypt in combination with amavis.

## Using authentication
For using the authentication add the following to gpgmailencrypt section in /etc/postfix/master.cf
-o smtp_sasl_auth_enable=yes / -o smtp_sasl_password_maps=hash:/etc/postfix/gpgmailencrypt_passwd

With /etc/postfix/gpgmailencrypt_passwd having the following structure
localhost user:password

Then use the following commands
sudo chmod 640 /etc/postfix/gpgmailencrypt_passwd / sudo postmap /etc/postfix/gpgmailencrypt_passwd

## Using starttls
Add the following to gpgmailencrypt section in /etc/postfix/master.cf:
-o smtp_use_tls = yes / -o smtp_tls_security_level = encrypt

## Using smtps
To use the gpgmailencrypt smtps feature with postfix 2.x you need to install stunnel (in Ubuntu the package is called stunnel4)
Create the file /etc/stunnel/gpgmailencrypt.conf
[gpgmailencrypt-smtps] / accept = 10000 / client = yes / connect = localhost:10028

And change /etc/default/stunnel4
ENABLED=1

Then start stunnel with
/etc/init.d/stunnel4 start

/etc/postfix/main.cf should be changed to
content_filter=gpgmailencrypt:[127.0.0.1]:10000

# The admin console
## The admin user – the hen and egg problem
First you have to create a normal user (which only the admin user can do), then you can give him administration rights.
So for the very first time you have to start the following python program as the user, that runs the gpgmailencrypt daemon. Replace “admin1” and “secreet” with the values you like
#!/usr/bin/python3 / import gpgmailencrypt / user=”admin1” / password=”secret” / with gpgmailencrypt.gme() as g: / g.adm_set_user(user,password)

Now the user is created.
Now change the /etc/gpgmailencrypt.conf to the following value
[daemon] / admins=admin1 #comma separated list of admins, that can use the admin console

Now restart the daemon, that's it.
## Using the admin console
Start
gme_admin.py localhost 10025

Replace 'localhost' and the port number with the values of your daemon
Now login as an admin user. You will see the following screen
Try to connect to localhost:10025 ... / gpgmailencrypt admin console / ============================ / User: admin1 / Password: / OK / Authentication successful. / Welcome. Enter 'HELP' for a list of commands / > _

The following commands are available:
flush	tries to re-send deferred e-mails
debug true/false	sets the debug mode valid options are / TRUE|FALSE, ON|OFF, YES|NO
deluser	deletes a user / example: 'deluser john'
help	Shows all available commands
messages	shows all systemwarnings and -errors
quit	leave the console
reload	reloads the configuration file
resetstatistics	sets all statistic values to 0
setuser	adds a new user or changes the password for an existing user / example: 'setuser john johnspassword'
statistics	print statistic information
users	print users

## Non-admin users
Users, that don't have the admin privilege can be used to login to the server, when the daemon need authentication, set with
/etc/gpgmailencrypt.conf
[daemon] / authenticate = True #users must authenticate

# Using gpgmailencrypt from the command line
Start
gme.py

The command line options are
Usage: / gme.py [options] receiver@email.address < Inputfile_from_stdin / Options: / -a --addheader: adds X-GPGMailencrypt header to the mail / -c f --config f: use configfile 'f'. Default is /etc/gpgmailencrypt.conf / -d --daemon : start gpgmailencrypt as smtpserver / -e pgpinline : preferred encryption method, either 'pgpinline','pgpmime' or / 'smime' / -f mail : reads email file 'mail', otherwise from stdin / -h --help : print this help / -k f --keyhome f: sets gpg key directory to 'f' / -l t --log t: print information into _logfile, with valid types 't' / 'none','stderr','syslog','file' / -n domainnames: sets the used domain names (comma separated lists, no space), / which should be encrypted, empty is all / -m mailfile : write email file to 'mailfile', otherwise email will be sent via smtp / -o p --output p: valid values for p are 'mail' or 'stdout', alternatively you / can set an outputfile with -m / -x --example: print example config file / -v --verbose: print debugging information into _logfile / -z --zip: zip attachments

# Using gpgmailencrypt as a module
import gpgmailencrypt / help(gpgmailencrypt)

The most important function is
gpgmailencrypt.encrypt_mails(self,mailtext,receiver)

An example:
import gpgmailencrypt / #reads the e-mail from a file / f=open(“myemail.eml) / mail=f.read() / f.close() / #sends an encrypted e-mail / with gpgmailencrypt.gme() as g: / g.encrypt_mails(mailtext=mail,recipient=”agentj@mib”) / #the following sends the e-mail to 2 recipients / g.encrypt_mails(mailtext=mail,recipient=[”agentj@mib”,”agentk@mib”])